## Slide 1: New Uploader for CODEX multicycle Data
Guolan Lu
5/26/2021

## Slide 2: Generate PSF for four filter channels
Use imageJ plugin PSF generator to generate 4 PSF for each filter:
http://bigwww.epfl.ch/algorithms/psfgenerator/
Parameters:
Keyence microscope:
  20x objective, NA 0.75, Working distance = 350 um
  XY resolution(pixel size) = 377.442 nm; Z-step = 1500 nm
  Wavelength (nm; excitation/emission): input emission wavelength
    DAPI: 358/425; GFP: 488/525; Cy3: 532/595; Cy5: 651/670
  Image size/tile: 1920 x 1440
  Number of z planes
  Display: grays
Save the PSF as the following names:
  PSF_BW_DAPI.tif
  PSF_BW_GFP.tif
  PSF_BW_Cy3.tif
  PSF_BW_Cy5.tif